GS110TP-100

Firmware Version V5.0.1.8

Known issues:

1. 	While the link is up, port cannot be removed from a VLAN if it is also member of a LAG.

Workaround: Remove the link or remove the port from the LAG first.

2. 	After setting the maximum number of allowed static locked MAC address to zero (under Security > Traffic Control > Port Security > Interface Configuration), no static MAC address can be added even when port security is disabled.

Workaround:  Change back the "Max Allowed Statically Locked MAC" from 0 to 20.

3. 	VLAN name cannot be changed to blank.

Workaround:  This is not service affecting.  If you really want to delete the VLAN name, please delete the VLAN first.  Then, recreate the VLAN without assigning a VLAN name.

- DNS setting will be lost if it restored from a configuration file followed by a system reboot.

Workaround:  None. It will be fixed in the next maintenance release.

Limitations:

None.