## Slide 1: DRAM BRING UP CONFIGURATION
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
Chia-Liang Hung
alexhung@realtek.com

## Slide 2: Introduction
Purpose
  This document will introduce how to use pre-calibration tool to figure out DRAM parameters
Preparation
  Documents
    DRAM Datasheet
    ‘CPU & Memory Controller Datasheet’, Realtek
  Image
    Pre-calibration image
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com

## Slide 3: Outline
DRAM Configuration
  Pre-Configuration
  DDR Pad Setting
  WRITE Timing Adjustment
  READ Timing Adjustment
  Memory Test and Restore Config
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com

## Slide 4: Configuration Flow
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
Figure. DDR bring up configuration flow
Pre-Configuration
DDR Pad Setting
READ Timing Adjustment
WRITE Timing Adjustment
Memory Test & Restore Config

## Slide 5: Configuration Tool
enter Preloader CLI
  press ‘.’ to trigger CLI before entry u-boot
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com

## Slide 6: Configuration Tool (cont.)
Using Preloader Configuration Tool
  modify configuration with dram/pll set commands
  *Note: more commands and related available value, please reference Appendix. Command List
  ‘call dram_setup’: apply modified DRAM configuration to control register and re-do calibration
  ‘call pll_setup’: apply modified PLL configuration to control register
  ‘save_para’: save current configuration back to flash
  ‘show dram_info’: show current DRAM configuration, not configuration in control register
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com

## Slide 7: Configuration Tool (cont.)
Frequency Modification
  Before DRAM bring up, DRAM frequency need to be check
  If frequency need to be modified, using pll set command
  and the do following steps to apply
    apply PLL configuration: ‘call pll_setup’
    apply DRAM configuration: ‘call dram_setup’
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
[ Related Commands]
get pll mem_clk
get pll cpu_clk
get pll lx_clk
get pll dsp_clk *if DSP exist
Note: unit is MHZ
[ Related Commands]
set pll clock <cpu_clk> <mem_clk> <lx_clk>
set pll clock <cpu_clk> <dsp_clk><mem_clk> <lx_clk> *if DSP exist
Note: unit is MHZ
Note: CPU, DSP, memory and LX related frequency could be found in CPU & Memory Controller Datasheet or Appendix . Suggested PLL Range

## Slide 8: Pre-Configuration
Step 1-1: Config DRAM Size and Bus Width
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
[ Related Commands]
set dram buswidth <value>
set dram size <value>
Pre-Configuration
DDR Pad Setting
READ Timing Adjustment
WRITE Timing Adjustment
Memory Test & Restore Config
Example 1-1:
DDR3 NANYA NT5CB128MHP: 256MB Bus Width=16
Using preloader CLI commands “set dram buswidth 16 “
“set dram size 256 “

## Slide 9: Pre-Configuration (cont.)
Step 1-2: Config DRAM AC Timing
  DTR0: tCAS, tWR, tCWL, tRTP, tWTR, tREFI
  DTR1: tRP, tRCD, tRRD, tFAWG
  DTR2: tRFC, tRAS
*Note: 1. pre-calibration tool will apply a safe DTR
configuration, or user can find out better
parameters according to DRAM datasheet
2. please reference next page for how to find
those parameters
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
Example 1-2: If DRAM frequency is 300MHz, 1 tCLK= 3.3ns
A. tRRD: according to spec, tRRD minimum requirement is 7.5ns
tRRD = 3 tCLK = 10ns > 7.5 ns
Using preloader CLI commands “set dram trrd 3 “
B. tREFI: according to spec, tREFI minimum requirement is 7.8us
If using tREFI = 3072 tCLK = 12*256 tCLK= 10.1 us > 7.8 us
Using preloader CLI commands “set dram trefi 12 “ and “set dram trefi_unit 256”
[ Related Commands]
set dram tcas <value>
set dram twr <value>
set dram tcwl <value>
set dram trtp <value>
set dram twtr <value>
set dram trefi <value>
set dram trefi_unit <value>
set dram trp <value>
set dram trcd <value>
set dram trrd <value>
set dram tfawg <value>
set dram trfc <value>
set dram tras <value>
* unit is tCLK

## Slide 10: Pre-Configuration (cont.)
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
How to find DTR parameters requirement in DRAM Datasheet?
4. Notice the units
3. Find the requirement value here according to different frequency
1. find AC Timing Table in DRAM datasheet
2. Using DTR related parameter as keyword
(Source is from NANYA DRAM DataSheet
Note: While DRAM frequency has been modified, DRAM AC Timing should be re-verified and configured.

## Slide 11: DDR Pad Setting
Step 2-1: Check signals amplitude and dc level
  WRITE: measure point is DRAM side
  READ: measure point is Chip Side
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
Chip
DRAM
Measure Point for WRITE
Measure Point for READ
Figure. DRAM Signal Measure Point
Pre-Configuration
DDR Pad Setting
READ Timing Adjustment
WRITE Timing Adjustment
Memory Test & Restore Config
[ Related Commands]
Continuous Read/Write:
call read_pattern <times>
call write_pattern <times> <pattern>
Single Read/Write:
lw <addr>
sw <addr> <value>
*Note: Those commands are applied to perform pure READ/WRITE

## Slide 12: DDR Pad Setting (cont.)
Step 2-2: if signals are below or above requirement, use command to change termination resistance value and re-check.
  Chip side
    ODT (On-Die-Terminate)
    OCD (On-Chip-Driver)
  DRAM side
    ODT and Dynamic ODT (Rtt_WR, DDR3 only)
    Driving strength
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
[ Related Commands]
Modify Chip side ODT/OCD:
set dram ctl_odt_ocd <odt> <ocd>
Modify DRAM side ODT/OCD:
set dram mrs_odt <value>
set dram mrs_rtt_wr <value> *only for DDR3
set dram drv_strength <value>
* unit is ohm
*Note: suggest to modify ODT first and then OCD

## Slide 13: DDR Pad Setting (cont.)
Example 2-1: CLK signal with/without DDR pad setting
  Using preloader CLI command “set dram ctl_odt_ocd 75 60”
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
odt: disabled
ocd: disabled
odt: 75 ohm
ocd: 60 ohm
*Note: Suggest Singal should be large than 1.1 V

## Slide 14: WRITE Timing Adjustment
Step 3: Do WRITE Delay Timing Adjustment
  DQS and Data signal alignment
  CLK and DQS signal alignment
  CLK and commands signal alignment
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
Chip
TX CLK
DRAM
CLK
DQS
DQS
DQn
DQn
WRITE
ADDR
D1
D0
[ Related Commands]
set dram clkm90_delay <value>
set dram dq_wr_delay_(0~15) <value>
[ Related Commands]
set dram clkm_delay <value>
[ Related Commands]
set dram tx_clk_phs_delay <value>
Pre-Configuration
DDR Pad Setting
READ Timing Adjustment
WRITE Timing Adjustment
Memory Test & Restore Config

## Slide 15: WRITE Timing Adjustment (cont.)
Step 3-1: DQS and Data signal alignment
  Verified signals: DQS and DQn
  < buswidth is 8-bits, DQ0~DQ7, buswidth is 16-bits, DQ0~DQ15 >
    * Note: At least, the longest and shortest DQ signal in PCB board should be verified
  Verified Timing Parameters
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
[ Related Commands]
DQS:
set dram clkm_delay <value>
DQn :
set dram clkm90_delay <value>
set dram dq_wr_delay_(0~15) <value>
DRAM Timing | Required (DDR3-800) |  | Measured
 | min | Max | 
DQ0~15 input setup time (tDS) | 125ps | - | 
DQ0~15 input hold time (tDH) | 150ps | - | 
*Note: In DRAM datasheet, please find required timing parameters according to different frequency

## Slide 16: WRITE Timing Adjustment (cont.)
Example 3-1
  Using preloader CLI command
  “set dram clkm_delay 0x5“
  and apply with “call dram_setup“
  Re-check waveform, DQS signal delays about 168 ps
  (tDH: 776 ps->944 ps)
  1 delay tap is about 30~40 ps
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
DQS0
DQ4
delay DQS0 signal
DQS0
DQ4
776 ps
944 ps

## Slide 17: WRITE Timing Adjustment (cont.)
Example 3-2: tDS, tDH measurement in DRAM 400MHz
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
DRAM Timing | Required (DDR3-800) |  | Measured
 | min | Max | 
DQ4 input setup time (tDS) | 125ps | - | 332ps
DQ4 input hold time (tDH) | 150ps | - | 776ps

## Slide 18: WRITE Timing Adjustment (cont.)
  Step 3-2: CLK and DQS signal alignment
  Verified signals: CLK and DQS
  Verified timing parameters
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
[ Related Commands]
set dram tx_clk_phs_delay <value>
DRAM Timing | Required (DDR3-800) |  | Measured
 | min | Max | 
DQS latching rising transitions to associated clock edge (tDQSS) | 0.25 tCK | 0.25 tCK | 
DQS falling edge to CK setup time (tDSS) | 0.2 tCK | - | 
DQS falling edge hold time from CK (tDSH) | 0.2 tCK | - | 
DQS input HIGH pulse width (tDQSH) | 0.45 tCK | 0.55 tCK | 
DQS input LOW pulse width (tDQSL) | 0.45 tCK | 0.55 tCK | 
*Note: Please find required timing parameters according to different frequency

## Slide 19: WRITE Timing Adjustment (cont.)
Example 3-3: tDQSS measurement in DRAM 400MHz
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
DQS0
CK
tDQSS should be within ¼ tCLK = 625 ps

## Slide 20: WRITE Timing Adjustment (cont.)
  Step 3-3: CLK and Commands signal alignment
  Verified signals: CLK and commands signals (RAS#, CAS#, CS# and )
  Verified Timing Parameters
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
[ Related Commands]
set dram tx_clk_phs_delay <value>
DRAM Timing | Required (DDR3-800) |  | Measured
 | min | Max | 
RAS# setup time (tIS) | 350 ps | - | 
RAS# hold time (tIH) | 275 ps | - | 
CAS# setup time (tIS) | 350 ps | - | 
CAS# hold time (tIH) | 275 ps | - | 
CS# setup time (tIS) | 350 ps | - | 
CS# hold time (tIH) | 275 ps | - | 
WE# setup time (tIS) | 350 ps | - | 
WE# hold time (tIH) | 275 ps | - | 

## Slide 21: WRITE Timing Adjustment (cont.)
Example 3-4: tIS measurement in DRAM 400MHz for CAS#
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
CAS#
CK
Command signals setup time value is 350 ps

## Slide 22: WRITE Timing Adjustment (cont.)
Example 3-4: tIH measurement in DRAM 400MHz for CAS#
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
CAS#
CK
Command signals hold time is 350 ps

## Slide 23: READ Timing Adjustment
Step 4-1: Apply configuration and do software calibration
with “call dram_setup” and check result is success
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
1. check result is success here
2. check frequency is correct
Pre-Configuration
DDR Pad Setting
READ Timing Adjustment
WRITE Timing Adjustment
Memory Test & Restore Config

## Slide 24: READ Timing Adjustment (Cont.)
Step 4-2: check READ Window result
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
Expected DQ READ Window
DDR frequency = 100 MHz
=> 0x001E0F00
DDR frequency = 200 MHz
=> 0x001E0F00
DDR frequency = 300 MHz
=> 0x001E0F00
DDR frequency = 400 MHz
=> 0x00150F00
[ Related Commands]
set dram dqs0_en_hclk/dqs1_en_hclk <value>
set dram dqs0_en_tap/dqs1_en_tap <value>
set dram dqs0_group_tap/dqs1_group_tap <value>
READ Window information

## Slide 25: READ Timing Adjustment (cont.)
Example 4-1 : DQn Falling Edge Result is not start from 0
using commands “set dram dqs0_en_hclk 0x1”
“set dram dqs1_en_hclk 0x1”
  “set dram dqs0_en_tap 0x7 “
  “set dram dqs1_en_tap 0x7”
  And do “call dram_setup” to apply
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com

## Slide 26: READ Timing Adjustment (cont.)
Example 4-2: DQn both rising and Falling Edge Result is not start from 0
  using commands “set dram dqs0_group_tap 4”
  “set dram dqs0_group_tap 4”
  And do “call dram_setup” to apply
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com

## Slide 27: Memory Test & Restore Config
Step 5-1: restore current DRAM parameters
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
show dram_info -u
Pre-Configuration
DDR Pad Setting
READ Timing Adjustment
WRITE Timing Adjustment
Memory Test & Restore Config
Notes: <number>

## Slide 28: Memory Test & Restore Config (cont.)
Step 5-2: Using command “exit” to enter u-Boot and do memory test by u-Boot command “mdram_test”
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
2. “mdram_test” to do memory test
1. “exit” to enter u-Boot
2. check frequency and size

## Slide 29: Memory Test & Restore Config (cont.)
Step 5-3: If memory test is passed
  copy previous DRAM parameters in step 5-1, and paste to soc_init_parameters.c to replace original parameters
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
1. Comment this line
2. Paste DRAM dump parameters here
3. Suggest to record DRAM frequency as a comment
soc_init_parameters.c

## Slide 30: Appendix. Command List
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
commands | available value | unit
set dram size <value> | 32/64/128/256/512/1024 | MB
set dram buswidth <value> | 8/16 | bits
set dram ctl_odt_ocd <value> | ODT: 24/25/30/40/50/60/75/80/100/150/160/200 OCD: 48/50/60/80/100/120/150/160/200/300/320/400 | Ohm
set dram tx_clk_phs_delay <value> | 0~31 | Taps
set dram clkm_delay <value> | 0~31 | Taps
set dram clkm90_delay <value> | 0~31 | Taps
set dram dq_wr_delay_(0~15) <value> | 0~31 | Taps
set dram dqm0/dqm1 <value> | 0~31 | Taps
set dram mrs_odt <value> | DDR2: 0/50/75/150, DDR3: 0/20/30/40/60/120 * 0 for disable | Ohm
set dram mrs_rtt_wr <value> | DDR3: 0/60/120, 0 for disable | Ohm
set dram mrs_drv_strength <value> | DDR2: 0: normal, 1: reduce DDR3: 0: 40 ohm, 1: 34 ohm | N/A

## Slide 31: Appendix. Command List (cont.)
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
commands | available value | unit
set dram dqs0_en_hclk <value> set dram dqs1_en_hclk <value> | 0: disable, 1: enable | N/A
set dram dqs0_en_tap <value> set dram dqs1_en_tap <value> | 0~31 | Taps
set dram dqs0_group_tap <value> set dram dqs1_group_tap <value> | 0~31 | Taps
call dram_setup | N/A | N/A
show <dram_info¦pll_info> [-u¦-p¦-v] | -p: preloader type, -u: TCL type, -v: verbose | N/A
show init_result | N/A | N/A
call write_pattern <times> <pattern> | times: <integer>, ex: 10000 pattern: <4 bytes string in Hex>, ex: 0xFF00FF00 | N/A
call read_pattern <times> | times: <integer>, ex: 10000 | N/A
get <dram¦pll> <parameter> |  | N/A
set pll clock <cpu-clk> <mem-clk> <lx-clk> set pll clock <cpu-clk> <dsp-clk> <mem-clk> <lx-clk> * if DSP exist | Reference to Appendix. Suggested PLL Range | MHz

## Slide 32: Appendix. Command List (cont.)
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com
commands | available value | unit
set dram tcas <value> | 2~11 | tCLK
set dram twr <value> set dram tcwl <value> | 1~8 | tCLK
set dram trtp <value> set dram twtr <value> | 1~16 | tCLK
set dram trp <value> set dram trcd <value> set dram trrd <value> set dram tfawg <value> | 1~32 | tCLK
set dram trefi <value> | 1~16 | tCLK
set dram trefi_unit <value> | 32/64/128/256/512/1024/2048/4096 | tCLK
set dram trfc <value> | 1~256 | tCLK
set dram tras <value> | 1~64 | tCLK

## Slide 33: Appendix. Suggested PLL range
Apollo
  CPU: 500~675 MHz, DSP: 500~550 MHz, Memory:100~400 MHz, LX: 200 MHz
  * Note: each frequency step is 25MHz
839x, 835x
  CPU: 400~750 MHz, Memory:100~400, LX: 50~200 MHz
  *Note: CPU, LX: each frequency step is 50MHz
  Memory: each frequency step is 25MHz
838x, 833x
  CPU: 300, 500 MHz, Memory: 193, 300 MHz, LX: 200 MHz
-<number>-
Copyright © 2013 Realtek Semiconductor Corp.
www.realtek.com